## Slide 1: Land Cover and Land Use (LCLU) applications
From ESA Advanced Training course on Land Remote Sensing by Mário Caetano

## Slide 2: Summary
Setting the scene: some definitions
LCLU mapping
The need for LCLU data
LCLU: a cross-cutting environmental variable
Relation between two European initiatives (GMES and INSPIRE) and LCLU LCLU and environmental legislation
LCLU and the DPSIR framework
At country level (the case study of the USA)
At European level (GSE Land and GMES FTS Land)
At Global level (GLG2000, MOD12Q1 and GLOBCOVER)
1
2
3

## Slide 3
Setting the scene: some definitions
LCLU mapping
The need for LCLU data
LCLU: a cross-cutting environmental variable
Relation between two European initiatives (GMES and INSPIRE) and LCLU LCLU and environmental legislation
LCLU and the DPSIR framework
At country level (the case study of the USA)
At European level (GSE Land and GMES FTS Land)
At Global level (GLG2000, MOD12Q1 and GLOBCOVER)
1
2
3

## Slide 4: A definition of land…
“'A delineable area of the earth's terrestrial surface, embracing all attributes of the biosphere immediately above or below this surface, including:
near surface climate,
soil and terrain forms,
surface hydrology including shallow lakes, rivers, marshes and swamps,
near-surface sedimentary layers and associated groundwater and geohydrological reserves,
plant and animal populations,
human settlement pattern and physical results of past and present human activity (terracing, water storage or drainage structures, roads, buildings, etc.)."
Source: Interdepartmental working group on land use planning -FAO (2004)

## Slide 5: Land cover versus Land use
Land cover (LC) - Physical and biological cover of the earth's surface including artificial surfaces, agricultural areas, forests, (semi-)natural areas, wetlands, water bodies.
Land use (LU) - Territory characterised according to its current and future planned functional dimension or socio–economic purpose (e.g. residential, industrial, commercial, agricultural, forestry, recreational).
Source: INSPIRE Directive
Functional definition of LU
description of land in terms of its socio-economic purpose (e.g. agricultural, residential, forestry)
LU can be inferred from LC
Sequential definition of LU
description of land based on series of operations on land, carried out by humans, with the intention to obtain products and/or benefits through using land resources.
LU cannot be inferred from LC. Other information sources are needed.

## Slide 6: A possible LC classification
Artificial surfaces
  Urban fabric
  Industrial, commercial and transport units o Mine, dump and construction sites
  Artificial, non-agricultural vegetated areas
Agricultural areas
  Arable land
  Permanent crops o Pastures
  Heterogeneous agricultural areas
Forests
(semi-)natural areas
  Scrub and/or herbaceous vegetation associations o Open spaces with little or no vegetation
Wetlands
  Inland wetlands
  Maritime wetlands
Water bodies
  Inland waters o Marine waters
Source: INSPIRE Drafting Team "Data Specifications“ (2007)

## Slide 7: A possible LU classification
Mining and Quarrying Manufacturing
Electricity, Gas and Water Supply Construction
The ISIC system for LU classification
17 sections, 60 divisions, 159 groups and 292 classes
Agriculture, Hunting and Forestry Fishing
Wholesale and Retail Trade, Repair of motor vehicles, motorcycles and Personal and household goods
Hotels and Restaurants
Transport, Storage and Communication Financial intermediation
Real estate, Renting and Business activities
Public Administration and Defense, Compulsory social security Education
Health and Social work
Other Community, Social and Personal Service Activities Private Households with Employed Persons
Extra-territorial Organizations and Bodies
Source: ISIC - International Standard Classification of all Economic Activities
The 17 sections of the first level characterize main economic activities.

## Slide 8: Summary
Setting the scene: some definitions
LCLU mapping
The need for LCLU data
LCLU: a cross-cutting environmental variable
Relation between two european iniciatives (GMES and INSPIRE) and LCLU LCLU and environmental legislation
LCLU and the DPSIR framework
At country level (the case study of the USA)
At European level (GSE Land and GMES FTS Land)
At Global level (GLG2000, MOD12Q1 and GLOBCOVER)
1
2
3

## Slide 9: The need for LCLU data
Biodiversity
LCLU
The most important environmental variable
Hydrology
Biogeochemical cycles
Natural disasters
Ecology
Climate change
Sustainability
Soil erosion
Land management
Epidemiology

## Slide 10: The need for LCLU data
Users of LCLU information
Policy makers
(e.g. DG from EC, EEA, National, Member States Agencies)
Agencies responsible for
policy implementation and enforcement
Research bodies
Industries and businesses that are often the target of policy
NGOs and the public
Information providers

## Slide 11
For many years the research emphasis has been on the classification step itself.
Image classification at pixel level
Map of categorical classes
Does it satisfy the user needs?
New classification algorithms
A new spatial unit of analysis
Spatial analysis for map generalisation
Recent research
Redefine the approach for thematic information extraction

## Slide 12
LCLU is recognised as one of the most important types of spatial data in two important European initiatives
GMES
Global Monitoring
for Environment and Security
ESA Web site
EC Web site
Directive 2007/2/EC
INSPIRE
Infrastructure for Spatial Information in the European Community
http://www.esa.int/esaLP/LPgmes.html http://www.ec-gis.org/inspire/ http://www.gmes.info/ or http://ec.europa.eu/gmes
COM (2004) 65 final – GMES: Establishing a GMES capacity by 2008 - (Action Plan (2004-2008))
COM(2005) 565 final - GMES: From Concept to Reality
COM(2008) 748 final - GMES: We care for a safer planet

## Slide 13: GMES
GMES is the European contribution to the Global Earth Observation System of Systems (GEOSS)
(in 2005 61 countries agreed on a 10-year
GEOSS implementation plan).
GMES is a joint initiative of the EC and the ESA, designed to establish a European capacity for the
operational delivery and use of information in support of Environment and Security policies.
It provides autonomous and independent access to information for policy-makers, particularly in relation to environment and security.
ESA implements the space component and the EC manages actions for identifying and developing services.
GMES will use, to the maximum extent possible, existing capacities in Member States or at European level.
GMES
Services
Space systems
In situ
systems
Data integration and information management

## Slide 14: INSPIRE INSPIRE is a Directive proposed by the EC in July 2004 setting the legal framework for the establishment and operation of an Infrastructure for Spatial Information in the European Community.
The purpose of INSPIRE is to support the formulation, implementation, monitoring activities and evaluation of Community policies and activities that may have a direct or indirect impact on the environment at various levels of public authority, European, national and local.
The components of INSPIRE infrastructures include: metadata; spatial data themes; spatial data services; network services and technologies; agreements on data and service sharing, access and use; coordination and monitoring mechanisms, processes and procedures.
INSPIRE should be based on the infrastructures for spatial information that are created and maintained by the Member States.
Member States will also ensure that the information is shared between public bodies and they would take steps to make geographical information more coherent.
Member States would make accessible their existing public sector geographical information over the INTERNET.

## Slide 15: INSPIRE
Building the European Spatial Data Infrastruture
Source: EEA

## Slide 16: The need for LCLU data
Landscape characterisation (composition, condition and dynamics)
LCLU data
Input for environmental models
Atmospheric emissions in air quality models
Potential for food production in models of food security
Fuel availability in models of wildfire risk
Ground permeability in flood risk models
As surrogate/proxies for other variables

## Slide 17
to help guide policy formulation and development
to help monitor and enforce the implementation of these policies
  to assess the impact of existing or planned policies
to maintain a watching brief in order to identify the need for new policy action
Ultimately
LCLU data is important for policy on environment
DPSIR system
has been widely adopted as a framework for policy analysis
The need for LCLU monitoring

## Slide 18: The need for LCLU data
Source: IG-LMCS (2007)
GMES Global Land Working Group, 2008
Ramsar Convention on Wetlands.
EU Policy areas
Environmental thematic strategies on urban environment, soil protection and sustainable use of natural resources;
Reporting obligations under the Water framework directive, management of Natura2000 sites,
Environmental impact assessments and reporting;
Regional policies, territorial cohesion and European spatial development perspectives;
Common Agricultural Policy (CAP);
Common Transport Policy;
EU Development Policies (i.e. sustainable development and poverty reduction, food security);
Infrastructure for spatial information in Europe – INSPIRE and ESDI.
International Environmental Agreements
the three Rio Conventions:
  UN Framework Convention on Climate Change (UNFCCC) and its Kyoto Protocol, o UN Convention to Combat Desertification (UNCCD),
  UN Convention on Biological Diversity (UNCBD),
the UN-ECE Long Range Transboundary Air Pollution Deposition and dispersion modelling,.
Other international conventions/agreements
UN Forum on Forest with the related “FLEGT ” policy whereby EU contributes to the transparency of the international timber market,
UN Millennium Development Goals, where Goal I pledges to improve food and nutrition security,

## Slide 19: The need for LCLU data
EU Policy and legal framework | Information requirement
Water Framework directive (2006-2015+) | Characterization of river catchment areas, prevention of groundwater pollution from diffuse and local soil contamination
Community Biodiversity Strategy (2006 – 2010+) Habitats directive Natura2000, 2010 target | Designated areas and habitats, change in ecosystems, fragmentation
Common Agriculture Policy (agri-environmental Regulation; New guidelines for Rural Development; CAP evaluations 2007-2013) | Landscape diversity and management, agriculture habitats, mapping rural area
Community Structural Policies (European Spatial Development Perspective –Territorial Cohesion; 2007-13 ) | Natural assets, land use conflicts, physical planning, territorial development
Follow up European Strategy for ICZM (2006+) | Land use and land cover change coastal zones
European Thematic Strategy on Urban Environment and sustainable land use (2006+) | Urban sprawl, rural-urban relationships
European Thematic Strategy on Soil Protection (2006+) | Soil degradation, protection and sealing
… | …
Source: EEA

## Slide 20: The DPSIR framework to report on environmental issues
LCLU data is needed throughout the entire DPSIR chain.
Source: EEA

## Slide 21: DPSIR for terrestrial environments
Driving Forces
Pressure
State
Impact
Responses
Source: EC (2004)

## Slide 22
Source: EC (2004)
The diversity of needs for LCLU information

## Slide 23: Summary
Setting the scene: some definitions
The need for LCLU data
LCLU: a cross-cutting environmental variable
Relation between two European initiatives (GMES and INSPIRE) and LCLU LCLU and environmental legislation
LCLU and the DPSIR framework
LCLU mapping
At country level (the case study of the USA)
At European level (GSE Land and GMES FTS Land)
At Global level (GLG2000, MOD12Q1 and GLOBCOVER)
1
2
3

## Slide 24: Summary
Setting the scene: some definitions
LCLU mapping
The need for LCLU data
LCLU: a cross-cutting environmental variable
Relation between two European initiatives (GMES and INSPIRE) and LCLU LCLU and environmental legislation
LCLU and the DPSIR framework
At country level (the case study of the USA)
At European level (GSE Land and GMES FTS Land)
At Global level (GLG2000, MOD12Q1 and GLOBCOVER)
1
2
3

## Slide 25: US National Land Cover Database (NLCD)
In 1992 several federal agencies of the US agreed to operate as a consortium in order to acquire satellite-based remotely sensed data for their environmental monitoring programs,
i.e. Multi-Resolution Land Characteristics Consortium (MRLC)
http://www.epa.gov/mrlc/ http://www.mrlc.gov/

## Slide 26: US National Land Cover Database (NLCD)
MCRL has been the umbrella for many US programs, which require landcover data for addressing their agency needs, namely the 2 National Land Cover Databases:
NLCD 1992
NLCD 2001
A single product: a land cover map
Vogelmann et al. (2001)
Multiple products: land cover map, percent tree canopy and percent urban impervious.
Homer et al. (2007)
NLCD 2006
Under development http://www.epa.gov/mrlc/nlcd-2006.html
NLCD 1992
NLCD 2001
NLCD 2006

## Slide 27: Thematic information extraction from satellite images
1
2
4
5
7
8
* mandatory
Geographical stratification
3 Image segmentation
6 Ancillary data integration
Post-classification processing
Definition of the mapping approach
*
Feature identification and selection
Classification
Accuracy assessment
*
*
*

## Slide 28: US National Land Cover Database (NLCD) - 2001
Source: Homer et al. (2004)

## Slide 29: US National Land Cover Database (NLCD) - 2001
Source: Homer et al. (2007)
Mapping Zone Input Layers
Decision Tree (See5)
Percent tree canopy
Land cover map
Percent urban impervious
Regression Tree (See5)

## Slide 30: US National Land Cover Database (NLCD) - 2001
Source: Homer et al. (2007)

## Slide 31: Summary
Setting the scene: some definitions
LCLU mapping
The need for LCLU data
LCLU: a cross-cutting environmental variable
Relation between two European initiatives (GMES and INSPIRE) and LCLU LCLU and environmental legislation
LCLU and the DPSIR framework
At country level (the case study of the USA)
At European level (GSE Land and GMES FTS Land)
At Global level (GLG2000, MOD12Q1 and GLOBCOVER)
1
2
3

## Slide 32
Source: IG-LMCS (2007)
http://www.gmes-geoland.info/ http://www.gmes-gseland.info http://www.gmes-forest.info/
Land in GMES

## Slide 33
GSE-Land (GMES Service Element Land)
GSE Land Services portfolio has been structured in four service areas:
Land Take monitoring -> Cohesion policies, ESDP, ESPON
Diffuse Pollution ->WFD, linking to CAP
Water Abstraction by Agriculture -> WFD, water management
UrbanAudit from DG ENV/DG REGIO
WFD – Water Framework Directive; ESDP - European Spatial Development Perspective, ESPON - European
Spatial Observatory Network
Source: http://www.gmes-gseland.info

## Slide 34
GSE Land - Regional Land cover map (M2.1)
Saar-Mosel catchment
Source data: Landsat 5 TM & Landsat 7 ETM+, or
SPOT 2,4,5 (10/20m multispectral, 5m PAN), or IRS 1C/D PAN and MS
Scale 1:50.000 ; MMU = 1 ha (artificial surface) and 5 ha (non artificial);
Source: http://www.gmes-gseland.info

## Slide 35
GSE Land - Urban Atlas
Madrid
Source data: SPOT 5 – XS (10m) and -PAN (2,5 m) Scale 1:10.000 ; MMU = 0,25 ha ; MDL = 10 m
Pre-processing, geocoding, segmentation, -classification, visual interpretation, accuracy assessment
The basic urban land use information is enhanced by soil sealing mapping (up to 11 classes).
Source: http://www.gmes-gseland.info

## Slide 36
Urban outline
Sealing levels
Spot-5 satellite image
GSE Land – soil sealing
Source: GSE-Land

## Slide 37
GSE Land - Urban audit indicators
“green urban area” and “public open areas” are extracted from the urban atlas and local population statistics.
Source: http://www.gmes-gseland.info

## Slide 38
Source: http://www.gmes-gseland.info
M2.6
inventory)
GSE Land
Land Take map (first
M2.4 Land Take map (change)
Source data: SPOT 5 MS; or SPOT 4 PAN or IRS PAN & LISS
Scale 1:25.000 ; MMU =
0,25 ha (artifical surface) and 1 ha (nonartificial); MDL = 10 m
Assessment of sealed surfaces concerning its relation to demographic data and trends during 3-5 years observation time.
Analysis is based on modelling of residential population distribution using EO derived sealing intensity and demographic data.
This information is combined with various datasets to illustrate its linkages with environmental pressures, trends in land consumption, and quality of life aspects.

## Slide 39
GMES Land Monitoring Core Service
The implementation of GMES started with three “Fast Track” Services (FTS) addressing Land Monitoring, Marine Monitoring and Emergency Response.
The goal of the GMES Land Monitoring Service is to provide timely, continuous and independent observations about the use of soil and other land resources and the changes of the land environment for responsible and farsighted policy-making at
all levels, from local to global.
Source: IG-LMCS (2007)

## Slide 40
GMES Land Monitoring Core Service
The GMES Land Monitoring Service includes:
Fast Track Services
  Continental component – a LC (+ changes) map for Europe
  Local component – high resolution maps of built-up areas
Service evolution
  Global component – e.g. land cover, biophysical parameters, and more thematic data on desertification, deforestation, food security
  Thematic layers – at both local and continental level, dedicated to specific European and MS policies (e.g. soil protection, agriculture, hydrological maps)
Source: IG-LMCS (2007)

## Slide 41: GMES FTS Land participating countries
38 countries with total area of 5.8 Mkm2
Source: ETC-LUSI (2007)

## Slide 42: GMES FTS Land products
CLC 2006
Built-up area / sealing
CLC Changes
Source: EEA

## Slide 43: GMES FTS Land products
GMES FTS Land resumes the tradition of the 1990 and 2000 CORINE Land Cover (CLC) databases
Thematic accuracy >85%
CLC map (CLC90; CLC2000 and CLC2006)
CLC changes (1990-2000 and 2000-2006)
MMU = 25 ha MMU = 5 ha
Methodology: computer assisted visual interpretation of satellite images Source data: CLC90 and CLC2000 Landsat MSS, TM and ETM+
CLC2006 SPOT-4 and IRS LISS III (dual date) Nomenclature: hierarchical with 44 classes
Source: EEA

## Slide 44
Intensification of agriculture
Urban sprawl
infrastructure development
A new dam
Source: ETC-LUSI

## Slide 45
Image2000
Image 2006
CLC2000
CLC-changes
Ancillary data
CLC2006
Ancillary data

## Slide 46
Natural vegetation
Agriculture with natural areas
Agriculture
Forest
21
33
4
12
18
8
19
6
10
12
4
9
Land cover change from 1985 to 2000 in Portugal (thousands of ha)
1
72
32
28
-1.1
-3.6
2.8
-8.6
-20.0
-10.0
0.0
10.0
20.0
Urban areas
50.0
41.2
40.0
30.0
Crescimento em relação a 1985 (%)
Natural vegetation
Urban areas
Agriculture
Forest
Agriculture with natural areas

## Slide 47
High-resolution layer for built-up areas 2000
CORINE Land Cover 2000 (100m grid)
Prague
Prague
 | Artificial surfaces
 | Non-artificial surfaces
Source: GSE SAGE; Producer: GeoVille / GISAT
Source: EEA

## Slide 48
High-resolution layer for built-up areas 2006
 | Artificial surfaces
 | Non-artificial surfaces
Source: EEA

## Slide 49
GMES
High resolution maps (built-up areas and forests)
CLC2006 (MMU=25 ha)
CLC-changes 2000-2006 (MMU=5ha)
FTS
LC map with approximately 20 classes with 1 ha (or less) MMU (updating periodicity – 3 to 5 years)
R&D
The goal: a GMES LAND MONITORING PILOT SERVICE by 2008
If LC-20 classes satisfies user requirements then it will replace the current CLC databases in 2010
Otherwise, CLC will be produced in 2010
Issues to be addressed in the development phase
automatic and robust land cover classification techniques at pan-European scale
use of multi-seasonal and multi-sensor images for improving the land cover classes discrimination
change detection tools which can be used to reduce the updating efforts
overall validation methods at pan-European level
aggregation/generalization techniques to move from local (MS) land cover/land use mapping to continental one

## Slide 50
GMES Land Monitoring Core Service
The GMES Land Monitoring Service includes:
(1) Fast Track Services
Continental component – a LC (+ changes) map for Europe
Local component – high resolution maps of built-up areas
Service evolution
  Global component – e.g. land cover, biophysical parameters, and more thematic data on desertification, deforestation, food security
  Thematic layers – at both local and continental level, dedicated to specific European and MS policies (e.g. soil protection, agriculture, hydrological maps)
Source: IG-LMCS (2007)

## Slide 51
the local component of the Core Service (CS) will produce update maps of the major European agglomerates, which could be used by the local authorities as input to maps of the noise intensity and noise dispersion in a DS.
Noise mapping
combining at parcel level land use information from the CS with agronomic models and diagnostic tools for farmers to optimise for example fertilizer input (DS).
Precision farming
DS which needs regular and accurate information on land use from the CS (irrigated/not irrigated crops) to better monitor irrigation at the level of water catchments.
Management of irrigation
the operational processing chain producing biophysical products and agro-meteorological indicators could be part of the Global Land component of the CS. Then the issuing of bulletin from expert knowledge is an added value product which could be part of a DS.
Crop Yield forecasts
GMES Land Monitoring Core Service
Examples of Downstream Services (DS) – Thematic layers

## Slide 52
near real time monitoring systems of environmental stress worldwide and slightly differed time monitoring systems of land cover and forest conversion.
Land cover and forest change
near real time monitoring system of natural carbon fluxes at the land-atmosphere interface.
Natural carbon flux
monitoring systems for the crop production and yield assessment to be operated in near real time, as an input to services in charge of common agricultural policy, food security and trade policies.
Crop production and food security
Soil and Vegetation variables: e.g. land cover, Leaf Area Index, vegetation fractional cover, burnt areas, surface reflectance.
Radiation variables : e.g. albedo, surface temperature, down welling radiation flux.
Water variables: e.g. soil moisture, evapotranspiration, etc...
Biogeophysical variables
GMES Land Monitoring Core Service
Global component

## Slide 53: Summary
Setting the scene: some definitions
LCLU mapping
The need for LCLU data
LCLU: a cross-cutting environmental variable
Relation between two European initiatives (GMES and INSPIRE) and LCLU LCLU and environmental legislation
LCLU and the DPSIR framework
At country level (the case study of the USA)
At European level (GSE Land and GMES FTS Land)
At Global level (GLG2000, MOD12Q1 and GLOBCOVER)
1
2
3

## Slide 54: Global land cover maps Images
Spatial resolution
References
Reference year
The 1st global LC map | AVHRR |  | 1º | DeFries and Townshend (1994)
- | AVHRR |  | 8 km | DeFries et al. (1998)
- | AVHRR |  | 1 km | Loveland et al. (2000)
MODIS LC map | MODIS | 2001 | 1 km | Friedl et al. (2002)
(MOD12Q1) |  |  |  | 
Global Land Cover 2000 (GLC2000) | VEGETATION | 2000 | 1 km | Bartholomé and Belward (2005)
GLOBCOVER | MERIS | 2005 | 300 m | Arino et al. (2007)

## Slide 55: GLOBCOVER
http://dup.esrin.esa.it/projects/summaryp68.asp

## Slide 56: GLOBCOVER The main goal of GLOBCOVER is to develop and demonstrate a service that will produce a global land cover map for 2005, using as main source of data MERIS full resolution data (300m)
A software system is being developed such that any further update of GLOBCOVER will be at recurrent cost.
GLOBCOVER is intended to update and to complement the other existing comparable global products such as GLC-2000.
GLOBCOVER is intended to improve previous global products, in particular through a finer resolution (300m)
The GLOBCOVER system
Source: Defourny et al. (2005)

## Slide 57: GLOBCOVER
Source: Arino et al. (2007)
MERIS FRS (Full resolution full swath) from Dec 2004 until June 2006 are used.
ESA made a considerable effort to improve geolocation accuracy.
Factors to take into account are the satellite attitude, relief deformation and the resampling procedure.
The goal is to have a positional accuracy better than 150m
bi-monthly mosaics
Temporal compositing generates seasonal and annual mosaics by averaging the monthly mosaics over the selected period.

## Slide 58: GLOBCOVER
It reduces the land cover variability
To improve discrimination efficiency of the classification algorithms
Stratification into equal-reasoning areas
Allows selection of region specific classification parameters (e.g., temporal synthesis, band combinations, number of classes)
Criteria
vegetation seasonality
snow cover
burning period
sun zenith angle
cloud coverage
data availability
Source: Defourny et al. (2005)

## Slide 59: GLOBCOVER
Step 1
Definition of homogenous land cover objects
Step 2
Derivation of neo-channels
Step 3
LC discrimination through iterative multidimensional clustering techniques (spectro-temporal classes)
Step 4
Clusters labeling using LCCS
Source: Defourny et al. (2005)

## Slide 60: GLOBCOVER
The nomenclature of GLOBCOVER is based on the Land Cover Classification System (LCCS) from FAO
http://www.glcn-lccs.org/
Global product – 22 land cover classes
Hierarchical tree from LCCS
Source: Bartholomé and Belward (2005)

## Slide 61: GLOBCOVER
http://ionia1.esrin.esa.int/

## Slide 62: GLOBCOVER
http://ionia.terradue.com/
European Space Agency Ionia GlobCover Portal
GlobCover products distributed as torrent files

## Slide 63: Land information services
http://www.land.eu/
The Land portal provides a common entry point to GMES data-sets across a variety of data repositories across Europe. The data-sets are contributed by EEA, JRC and the GMES projects geoland, Boss4GMES, GSE Forest Monitoring, GSE Land Information Services
http://www.land.eu/portal

## Slide 64: Summary
Setting the scene: some definitions
LCLU mapping
The need for LCLU data
LCLU: a cross-cutting environmental variable
Relation between two european iniciatives (GMES and INSPIRE) and LCLU LCLU and environmental legislation
LCLU and the DPSIR framework
At country level (the case study of the USA)
At European level (GSE Land and GMES FTS Land)
At Global level (GLG2000, MOD12Q1 and GLOBCOVER)
1
2
3

## Slide 65: References Arino, O. et al., 2007, GlobCover: ESA service for Global Land Cover from MERIS. Proceedings of IGARSS’2007, Barcelona (Spain), 23-27 July, 2007.
Bartholomé, E., and Belward, 2005, GLC2000: a new approach to global land cover mapping from Earth observation data. International Journal of Remote Sensing, 26(9): 1959-1977.
Bartholomé, E., Belward, A.S., Achard, F., Bartalev, S., Carmona-Moreno C., Eva, H., Fritz, S., Grégoire, J.-M., Mayaux, P. And Stibig, H.-J., 2002, GLC2000—Global Land Cover Mapping for the Year 2000—project Status November 2002. Publications of the European Commission, EUR 20524 EN (Luxembourg: Office for Official Publications of the European Communities).
Defourny, P., Vancutsem, C., Bicheron, P, Brockmann, C., Nino, F., Schouten, L., Leroy, M., 2006, GLOBCPVER: a 300m global land cover product for 2005 using ENVISAT MERIS Time Series, Proceedings of ISPRS Commission VII Mid-Term Symposium: Remote Sensing: from Pixels to Processes, Enschede (NL), 8-11 May, 2006.
DeFries, R. S., & Townshend, J. G. R., 1994, NDVI derived land cover classifications at a global scale. International Journal of Remote Sensing, 5: 3567– 3586.

## Slide 66
DeFries, R., Hansen, M., Townsend, J. G. R., and Sohlberg, R., 1998, Global land cover classifications at 8 km resolution: the use of training data derived from Landsat imagery in decision tree classifiers. International Journal of Remote Sensing, 19: 3141– 3168.
Duhamel, C., 1998, First approximation of a reference land use classification, Report to the FAO.
EC, 2004, Building a European information capacity for environment and security. A contribution to the initial period of the GMES Action Plan (2002-2003).
Friedl, M.A., Mciver, D.K., Hodges, J.C.F., Zhang, X.Y., Muchoney, D., Strahler A.H., Woodcock, C.E., Gopal, S., Schneider, A., Cooper, A., Baccini, A., Gao, F. And Schaaf, C., 2002, Global land cover mapping from MODIS: algorithms and early results. Remote Sensing of Environment, 83: 287–302.
GSE Land Team, 2006, GSE Land Service Prospectus; ITD-0421-RP-0013-S3.
GMES Global Land Working Group, 2008, Global component of the GMES Monitoring Core Service
Homer et al., 2007, Completion of the 2001 National Land Cover Database for the Counterminous United States. Photogrammetric Engineering and Remote Sensing, 73(4) 337-341.

## Slide 67
Homer, C. C. Huang, L. Yang, B. Wylie and M. Coan. 2004. Development of a 2001 National Landcover Database for the United States. Photogrammetric Engineering and Remote Sensing, 70 (7): 829-840
INSPIRE Drafting Team "Data Specifications“, 2007, Definition of Annex Themes and Scope.
IG-LMCS (Implementation Group on GMES Land Monitoring), 2007, GMES Fast Track Land Monitoring Core Service Strategic Implementation Plan.
Loveland, T. R., Reed, B. C., Brown, J. F., Ohlen, D. O., Zhu, Z., Yang, L., and Merchant, J. W., 2000, Development of a global land cover characteristics database and IGBP DISCover from 1 km AVHRR data. International Journal of Remote Sensing, 21(6–7): 1303– 1365.
United Nations, International Standard Industrial Classification (ISIC), Rev. 3 http://unstats.un.org/unsd/cr/registry/regcst.asp?Cl=2
Vogelmann JE, Howard SM, Yang L, Larson CR, Wylie BK and Van Driel N., 2001, Completion of the 1990s National Land Cover Data Set for the Conterminous United States from Landsat Thematic Mapper Data and Ancillary Data Sources. Photogrammetric Engineering and Remote Sensing, 67:650-662